## Slide 1: Multi-fidelity Surrogate Modeling for Application/Architecture Co-design
Yiming Zhang1, Aravind Neelakantan2, Nalini Kumar2, Chanyoung Park1 Raphael T. Haftka1, Nam H. Kim1, Herman Lam2
1Department of Mechanical and Aerospace Engineering
2Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida 32611

## Slide 2: Introduction
Goal
Reduce computational budget of HPC codes (parent app)
  Using representative apps (mini-apps, skeleton apps)
  For application/architecture co-design
Low-cost model validation over larger design space
  Quantitatively
Performance prediction of parent app
Parent app
Mini-app
Skeleton app
How representative are we of each other?

## Slide 3: Combining Multi-fidelity Predictions
Approach
How to combine predictions with different fidelity?
  Probabilistic modeling to quantify the relation
  Expect improved accuracy with low cost/time
Cost/ Time
Experiments
Accuracy for simulating physical phenomenon
Analytical models
Low-fidelity
High-fidelity
Simulations
Combining simulations and experiments
Illustration of MFS

## Slide 4: Co-Design Using Behavioral Emulation (BE)
Simulation Platforms
BE SST
FPGA Acceleration
BE Simulation
HW/SW co-design
  Algorithmic & architectural design-space exploration (DSE)
BE is coarse-grained simulation
  Balance of simulation speed & accuracy for rapid design-space evaluation
* BEO – Behavioral Emulation Object
Coarse-grained
Simulation Platforms

## Slide 5: Behavioral Emulation with MFS
Objective
Reduce computational budget by fitting BE simulation to CMT-nek using Multi-Fidelity Surrogate (MFS) – current work
Extrapolation of CMT-nek towards large-scale runs using BE and MFS – extended work (email me for more details)

## Slide 6: Application Case Study*
Parent app – CMT-nek
  Perform simulation of instabilities, turbulence, and mixing in particulate-laden flows under conditions of extreme pressure and temperature
  Developed from Nek5000 - open-source software for simulating unsteady incompressible fluid flow with thermal and passive scalar transport
Mini-app – CMT-bone
  Key data structures and compute and communication kernels of CMT-nek
  Simplifies number of computation and communication operations performed at each time step in simulation
Skeleton app – CMT-bone-BE
  Key compute kernels & comm. patterns that affect performance
  Abstract, modular, easy to modify & instrument for rapid algorithmic DSE
* All applications developed at PSAAP-II Center for Compressible Multiphase Turbulence (CCMT) at University of Florida

## Slide 7: Developing MFS: Experimental setup
Element Size
Number of processors
Elements per processor
Design of experiment (DOE)
  Element size (ES) = 5,9,13,17,21
  Elements per processor (EPP) = 8,32,64,128,256
  Number of processors (NP) = 16,256,2048,16384,131072
125 total data points
  * BE simulation: all 125 runs
  CMT-nek: 22 runs
  CMT-bone: 67 runs
Multi-fidelity surrogate model
  Fitting CMT-nek using corrected fitting of BE simulation
  For large problems, low-fidelity BE simulation is computationally cheaper than high-fidelity CMT-nek or CMT-bone

## Slide 8: Least Squares MFS
Translate LF data against few HF data
  Linear regression with multi-fidelity data as basis for predictions
Robust with noise effect
Form of translation function
Schemes to determine surrogate parameters
Selected a popular form with a scale factor and a discrepancy surrogate
Bayesian vs. Deterministic
Spatial distribution vs. Residual error
Sequential vs. Simultaneous
Heuristic vs. Analytical
Developed a multi-fidelity surrogate for improved robustness and accuracy

## Slide 9: HPC system under study
Vulcan @ LLNL
  IBM BG/Q architecture
  16 cores/node, 24k nodes, 390k cores
  16GB memory/node, 400TB compute memory

## Slide 10: Validation: BE Simulations vs CMT-bone-BE
Measured
Simulating a bigger system than Vulcan (512k cores)
Average % error between CMT-bone-BE simulation and execution time is 4%
Maximum error is 9%
BE Simulation
CMT-bone-BE (Skeleton app) Execution
element size
100 runs & 100 simulations

## Slide 11: Validation: CMT-bone vs CMT-bone-BE
Comparing the trend under same experimental setup
Observation
  Different ranges of execution time
    CMT-bone-BE (skeleton app) is computational cheaper than CMT-bone
  Similar trends between CMT-bone-BE and CMT-bone
    Execution time monotonically increases for both with change in ES and EPP
    Color scales on both graph verify the similarity on trend

## Slide 12: Evaluating MFS Predictions
3 case studies
  Multi-fidelity model based mostly on BE simulation (LF) and few CMT-nek (HF parent app) data points to predict the performance of CMT-nek (HF)
  Multi-fidelity model based mostly on BE simulation (LF) and few CMT-bone (relatively HF mini-app) data points to predict performance of CMT-bone (HF)
  Multi-fidelity model based mostly on CMT-bone (relatively LF mini-app) and few CMT-nek (HF) data points to predict performance of CMT-nek (HF)

## Slide 13: Case 1: CMT-nek (HF) vs BE simulation (LF)
Accuracy of corrected BE simulation at 10 left-out CMT-nek test points
  Overall error (RMSE) is less than 8% with 10 or more nek data (left figure)
  Max error is less than 15% with 10 or more CMT-nek data (right figure)

## Slide 14: Case 2: CMT-bone (HF) vs BE simulation (LF)
Accuracy of corrected BE simulation at 20 left-out CMT-bone test points
  Overall error (RMSE) is less than 10% with 10 or more CMT-bone data (left figure)
  Max error is less than 20% with 9 or more CMT-bone data (right figure)

## Slide 15: Case 3: CMT-nek (HF) vs CMT-bone (LF)
Accuracy of corrected BE simulation at 10 left-out CMT-nek test points
  Overall error (RMSE) is less than 10% with 3 or more nek data (left figure)
  Max error is less than 25% (at the 10 test points) with 9 or more nek data (right figure)
  The jump after 9 points is due to over-fitting

## Slide 16: Evaluating MFS Predictions – Summary
LS-MFS was very accurate with less than 8% error
  Based on typical set of 12 samples
  For all the 3 case studies
Case 3 has more prediction error compared to case 1
  Scarce CMT-bone samples (67 runs - LF data in case 3) compared BE simulation (125 runs - LF data in case 1)
  Residual errors of supports this observation

## Slide 17: Conclusion and Future Work
Performed quantitative validation at reduced computational budget using least square MFS
  Less than 8% error (RMSE) in all three case studies
Demonstrated extrapolation
  Email me for more details
Future work
  Comparing different MFS framework – LS-MFS, co-Kriging, etc.
  Extrapolation with more data points
  Explore other effective design of experiments

## Slide 18: Do you have any questions?
aravindneela@ufl.edu